## Slide 1: CS 31006: Computer Networks – The Data Link Layer

## Slide 2: The Data Link Layer
Physical
Data Link
Network
Transport
Application
Logical Link Control
Medium Access Control

## Slide 3: Every Layer Adds Up Their Own Services
Data Link
Network
Addressing
Routing
Framing and Access Control
Error Control
Flow Control
Switching
Physical
AD/DA Conversion
Modulation
Coding
Analog Communication
MAC
LLC

## Slide 4: Data Link Layer Switching
Connect multiple LANs together
Do not send traffic onto ports where it is not needed
  Each LAN can run at full speed

## Slide 5: Data Link Layer Switching
Data link layer switches (sometime called as bridge – the old name) should be completely transparent
  Plug and Play – no address change
  The operations of existing LANs should not be affected
  The functionality of the devices should remain same even if they are part of the switched LAN
  Easy to move stations over a switched LAN similar to a normal LAN
Step 1: Learning switches (backward learning algorithm) to stop traffic being sent where it is not needed
Step 2: Spanning tree algorithm to break loops

## Slide 6: Learning Switches / Bridges
Collision Domain - 1
Collision Domain - 2
The old topology – not used now a days
This topology is mostly used
- Single machine at every switch port

## Slide 7: Learning Switches / Bridges
Switch operates in promiscuous mode
  Accepts every frame transmitted by stations attach to each of its ports
The switch decides whether to forward or discard each frame, and if forward which port to output the frame
Maintain a table (Output Port, MAC address) that maps at which port what machine / machines are connected
When the switches are first plugged in, the table is empty

## Slide 8: Learning Switches/ Bridges
Use flooding at the initialization – every incoming frame for an unknown destination is output on all the ports of the switch, except the one from where the frame has arrived
Every network interface (machine) connected on that receives that frame
  Decode the frame
  Check the destination MAC address at the frame header
  If the address matches, accept the frame
  Else, drop the frame
The switches starts learning about the (Output Port, MAC address) at this phase – called the backward learning

## Slide 9: Learning Switches / Bridges
For every incoming frame at a port, check the source MAC address
  If the destination MAC is that one, then the frame needs to output at the same port
The (Output port, MAC address) table is populated gradually by applying this backward learning
Port A
Source = MAC1 Destination = MAC2

## Slide 10: Learning Switches / Bridges
For every incoming frame at a port, check the source MAC address
  If the destination MAC is that one, then the frame needs to output at the same port
The (Output port, MAC address) table is populated gradually by applying this backward learning
Port A
Source = MAC1 Destination = MACx
Port A, MAC1

## Slide 11: Learning Switches / Bridges
For every incoming frame at a port, check the source MAC address
  If the destination MAC is that one, then the frame needs to output at the same port
The (Output port, MAC address) table is populated gradually by applying this backward learning
Port A
Port A, MAC1
Source = MACx Destination = MAC1
Delete old entries if not used for some time

## Slide 12: Learning Switches / Bridges – The Rules / Mechanism
If the port for the destination address is the same as the source port, discard the frame
If the port for the destination address and the source port are different, forward the frame on the destination port
If the destination port is unknown, use flooding and send the frame on all ports except the source port
Source: Computer Network, Tanenbaum, Wetherall, The Medium Access Control Sublayer, Section 8

## Slide 13: Cut Through Switching
The procedure needs to be very fast - switches are technically observing all the frames coming through
Implement in hardware
Once you start getting the bit stream, decode them immediately based on MAC frame structure
  Observe the source MAC and destination MAC
  Based on the destination MAC, if the switch does not need to forward the frame, do not process it further
Also known as wormhole routing

## Slide 14: Spanning Tree Switches
To increase reliability, redundant links may be deployed between the switches
Creates loop in the topology
Note that for unknown destination, switches flood the frames
Such frames can loop within the LAN

## Slide 15: Spanning Tree Switches
Construct a spanning tree across the switches
B1
B2
B3
B4
B5
B6

## Slide 16: Spanning Tree Protocol (STP)
Switches run a distributed algorithm to build the spanning tree
Each switch periodically broadcast a configuration message out all of its ports , processes the message it receives from other switches
  Embedded in STP frames
To choose the root of the spanning tree, the switches include an identifier based on the MAC address in the configuration message, as well as the identifier they believe to be the root
The bridges choose the bridge with the lowest identifier to be the root

## Slide 17: Spanning Tree Protocol (STP)
A tree of shortest paths from the root to every switch is constructed
  Include the distance from the root in the configuration messages
Each switch remembers the shortest path it finds to the root
The switches then turn off ports that are not part of the shortest path
The algorithm continues to run to detect any changes in the topology and update the tree

## Slide 18: Spanning Tree Protocol (STP)
Invented by Radia Perlman, 1985 (sometime called as “Mother of Internet”)
“I think that I shall never see A graph more lovely than a tree. A tree whose crucial property Is loop-free connectivity. A tree that must be sure to span So packets can reach every LAN. First, the root must be selected. By ID, it is elected. Least-cost paths from root are traced. In the tree, these paths are placed. A mesh is made by folks like me, Then bridges find a spanning tree.”
-Radia Perlman

## Slide 19: Network Devices at Different Layers
Repeater, Hub
Bridge, Switch
Router
Transport Gateway
Application Gateway
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Application Layer

## Slide 20: Virtual LAN (VLAN)
Image Source: https://www.cisco.com
LAN is a broadcast domain
  Every frame is a broadcast to all the machines connected in a switch port
VLAN
  Construct a broadcast domain even if they are not a part of the switch port – use VLAN ID
  Logical segmentation
  Better security, Ex. Design policy such that only the nodes in a VLAN can communicate with each other

## Slide 21: VLAN Support in 802.1Q

## Slide 22: Error Detection and Correction
Bit errors can be introduced during transmission of the signal – more common for wireless networks
Add redundant information with the frame that is sent
Error detection: Include enough redundancy so that the receiver can separate out a correct frame and an erroneous frame (cannot identify the actual error)
Error correction: Include enough redundancy so that the receiver can correct errors up to some level (detect which bits are having an error)

## Slide 23: Error Detecting Codes - Parity Bit
Include a single parity bit with the data.
The parity bit is chosen so that the number of 1 bits in the codeword is even (or odd, depending on the setup)
  1101110011 is the data to transmit
  Codeword is 11011100111 for even parity transmission
Can detect an odd numbers of bit errors – single bit error can be reliably detected
  Difficult to detect for burst error

## Slide 24: Error Detecting Codes – Interleaving Parity
Source: Computer Network, Tanenbaum, Wetherall, The Data Link Layer, Section 2
Even parity
N parity bits are used for kN data bits
k bit errors will be reliably detected with at most one error per row

## Slide 25: Error Detecting Codes – Checksum
Let us look into the case for 16-bit Internet checksum
Divide the data bits into 16 bit words
Use 1’s complement arithmetic to compute the sum
Find out 1’s complement of the result - that’s the checksum

## Slide 26: Example – 8 bit Checksum
Say, we want to transmit 1101110011001110
Two 8 bit words – 11011100 and 11001110
1’s complement addition - 00111100
1’s complement of the results – 11000011 – that’s the checksum
More rigorous than parity check – two bit flipped remains undetected in parity check, but may be detected in checksum

## Slide 27: Error Detection Code – Cyclic Redundancy Check (CRC)
Also known as polynomial code – treat bit stream as a representation of polynomials with coefficient 0 and 1
For example, 1011001 can be treated as 1.x6 +0.x5 +1.x4 +1.x3 +0.x2 +0.x1 +1.x0, which is equivalent to x6+ x4+ x3+1
The sender and the receiver must agreed upon a generator polynomial G(x)
  Both the high and the low order bits for the generator polynomial must be 1
To compute CRC for a polynomial M(x) corresponds to a frame, the number of bits in the frame must be longer than the generator polynomial

## Slide 28: Error Detection Code – Cyclic Redundancy Check (CRC)
Append CRC at the end of the frame, such that the polynomial represented by the CRC included frame must be divisible by G(x)
The receiver checks whether the received frame is divisible by G(x), if no, then there has been a transmission error

## Slide 29: Error Detection Code – Cyclic Redundancy Check (CRC)
Let r be the degree of G(x), append r zero bits to the low order end of the frame, so the frame contains m+r bits where m is the number of bits in the original frame. The polynomial corresponds to xrM(x)
Divide the bit string corresponds to xrM(x) by the bit string corresponding to G(x) using modulo 2 division
Subtract the remainder (which is always r bits or fewer) from the bit string corresponding to xrM(x) using modulo 2 subtraction. The result is the checksum frame to be transmitted
  Subtraction is equivalent to XOR in modulo 2 arithmetic

## Slide 30: CRC – Example
Source: http://computing.dcu.ie/~humphrys/Notes/Networks/data.polynomial.html
A polynomial code with r check bits can detect all burst errors less than on equal to r

## Slide 31: Forward Error Correction (FEC)
Let a frame consists of m data bits and r check bits
Block codes: The r check bits are computed solely as a function of the m data bits
Linear codes: The r check bits are computed as a linear function of the m data bits, example: XOR with modulo 2 arithmetic
Error correcting codes – the r check bits that are sent with the data bits for correcting a single or multiple bit errors during the transmission

## Slide 32: Hamming Distance
The number of bit positions in which two codeword differs (Hamming, 1950)
Example
Codeword-1 11001101
Codeword-2 01001010
XOR 10000111
Hamming distance is 4
If two codewords are a Hamming distance d apart, it will require d single bit errors to convert one into another

## Slide 33: Hamming Distance for Error Detection
Number of possible m bit data messages 2m
Number of possible m+r codewords 2m+r – all the codewords are not valid codewords
  We can have 2m different codewords corresponding to 2m different messages
To detect d bit errors, we need to ensure that the Hamming distance between two valid codewords is d+1
d

## Slide 34: Hamming Distance for Error Correction
We need to map every invalid codeword to a valid codeword
To correct d single-bit errors, the minimum Hamming distance between two codewords should be at least 2d+1
d
d
2d + 1

## Slide 35: Hamming Distance for Error Correction - Example
Consider the four codewords
  0000000000
  0000011111
  1111100000
  1111111111
The hamming distance is 5 – we can correct single and double bit errors
If the received codeword is 1010100000, we can expect the original codeword be 1111100000
Say you have received 1010000000, and there are maximum three bit errors, guess the original codeword

## Slide 36: Hamming Codes - Encoding
Say the data is 1000001
11 = 1 + 2 + 8
10 = 2 +8
9 = 1 + 8
7 = 1 + 2 + 4
6 = 2 + 4
5 = 1 + 4
3 = 1 + 2
P1 | P2 | M3 | P4 | M5 | M6 | M7 | P8 | M9 | M10 | M11
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1
2x positions are for parity bits, rest for data bits
Gives a code with Hamming distance of 3
One bit error can be corrected

## Slide 37: Hamming Codes – Decoding with Single Bit Error
Single bit error in data bit
11 = 1 + 2 + 8
10 = 2 +8
9 = 1 + 8
7 = 1 + 2 + 4
6 = 2 + 4
5 = 1 + 4
3 = 1 + 2
P1 | P2 | M3 | P4 | M5 | M6 | M7 | P8 | M9 | M10 | M11
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
Check the parity bits
We can find out an error in M5

## Slide 38: Hamming Codes – Decoding with Single Bit Error
Single bit error in parity bit
11 = 1 + 2 + 8
10 = 2 +8
9 = 1 + 8
7 = 1 + 2 + 4
6 = 2 + 4
5 = 1 + 4
3 = 1 + 2
Check the parity bits
We can find out a mismatch at M7, M6 and M5
We can correct at most one bit error
P4 is the common parity bit – so the error is there
P1 | P2 | M3 | P4 | M5 | M6 | M7 | P8 | M9 | M10 | M11
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 39: Framing
Identify a frame from the received bits
How do you you identify which part of the bit stream is a single frame?
Can you use a length field in the header?
00110101000100010

## Slide 40: Flag bits at the Beginning of the Frame
Start frame delimiter (SFD) and end frame delimiter (EFD)
A special bit sequence indicating beginning of a frame
EFD is deprecated and is not used now a days
Ethernet SFD: 10101011
Preamble: Synchronize the sender and the receiver – sequence of 10101010

## Slide 41: Ethernet Frame Structure

## Slide 42: Byte Stuffing (PPPoE)
10101011 can also be a part of the payload
Solution: Insert a special escape byte (ESC) if the SFD is part of the data – used in Point to Point Protocol (PPP)
ESC can be part of the data as well – insert another ESC before the ESC
A
SFD
B
A
ESC
SFD
B
A
ESC
B
A
ESC
ESC
B

## Slide 43: Bit Stuffing (HDLC)
Byte stuffing has the overhead of one byte per ESC character
Use bit stuffing instead of byte stuffing – implemented in High-level Data Link Control (HDLC) protocol
In HDLC, each frame begins and ends with 01111110 (called FLAG byte)
Six consecutive 1’s in the data can get confused with this FLAG byte
Stuff a 0 bit if there is 5 consecutive 1’s in the data bit – transmit 011111010 instead of 01111110

## Slide 44: Bit Stuffing Example

## Slide 45: The Channel Allocation Problem
Many of the times, the media is a broadcast media
A wireless Network
A Cellular Network

## Slide 46: Static Channel Allocation
Frequency Division Multiple Access (FDMA):
Time Division Multiple Access (TDMA):

## Slide 47: Dynamic Channel Allocation
Static Channel Allocation has multiple problems:
  Resource wastage when the user is idle
  Strong synchronization is necessary
Dynamically allocate channels to the end users whenever required – multiple access protocols
Probabilistic scheduling among devices or users - contention based systems
  Schedule the nodes such that contention can be minimized

## Slide 48: Multiple Access Protocol
Pure Aloha: Transmit the frame whenever you have one
  Results in collision
  The hub rebroadcast the frame ( works as an acknowledgement)
  If the sender does not hear its frame within a timeout, retransmission the frame again
Slotted Aloha: Divide time into discrete interval called slots. Transmit the frame at the beginning of the next slot
  The users need to agree on slot boundaries
  Collision can still happen, retransmit after timeout
  Doubles up the efficiency compared to pure Aloha – check the Tanenbaum book for details !
Best channel utilization with slotted aloha is 1/e (e=2.71828), approx. 36.7%

## Slide 49: Carrier Sense Multiple Access (CSMA)
Physical carrier sensing (PCS): Sense the carrier to see whether there is any ongoing signal.
If PCS returns the channel to be idle, the station sends data
Otherwise wait until the channel becomes idle
If collision occurs, wait for random amount of time and repeat the process
We call this as 1-persistent CSMA

## Slide 50: p-persistent CSMA
Divide the time to logical slots
When station is ready to send a frame, sense the channel (PCS)
If the channel is idle at the current slot, then transmit with probability p
With probability 1-p, target the next slot, and repeat the process
Non-persistent CSMA: If the channel is sensed busy through PCS, wait random amount of time, and then sense again

## Slide 51: Collision in CSMA (CSMA/CD)
Two stations may sense the channel idle at the same time, and starts transmission
A collision can happen in the channel – detect the collision
  Collision signal will differ from the normal signal
Random Back-off: Wait for random amount of time if a collision is detected
Binary Exponential Back-off: At nth attempt, wait for time equivalent of random(0,2n-1) slots

## Slide 52: Collision Detection and its Impact over MAC Frame Length
Worst case collision detection time = 2 x propagation delay
To detect a collision, the minimum frame transmission time should be equal to 2 x propagation delay (eg. Minimum Ethernet frame size = 64 bytes)

## Slide 53: Ethernet Performance - Contention Interval
Contention interval is the time when the channel bandwidth is not utilized due to collision
We need to estimate the probabilistic length of a contention interval

## Slide 54: Ethernet Performance
stations are ready to transmit. Each station transmits during a contention slot with probability
Consider a given slot. What is the probability that some station acquires the channel in that slot?
is maximized when , with as
The probability that the contention interval has exactly slots in it is
What is the mean number of slots per contention?

## Slide 55: Ethernet Performance
Let be the propagation delay, a slot duration is set to to ensure collision detection within the slot duration.
We observed that mean number of slots per contention is
Mean contention interval
We observed that with optimal , , So, the maximum value of is

## Slide 56: Ethernet Performance
Mean frame transmission duration is
Channel efficiency =
Image Source: Computer Networks, Tanenbaum

## Slide 57: Can You Detect Collision over Wireless?
Wireless Signal
  Fading – Attenuation is high, Signal strength drops as the signal propagates
  Shadowing – Gets affected by shadowed textures, like wall
  Multipath Propagation – Reflected signals may come from different directions
Additive Interference: Signals from multiple sources gets added up and interfere with the communication of a third device
  Individual signals may not enough for interference
Interference range is different from the transmission range

## Slide 58: Hidden Terminal Problem
Image Source: https://www.youtube.com/watch?v=X-H2tLesBUQ

## Slide 59: Exposed Terminal Problem
Image Source: https://en.wikipedia.org/wiki/Exposed_node_problem

## Slide 60: Wireless Scenario
Collision detection is not feasible for wireless
How will detect a data loss due to interference?
  Sender transmits a DATA
  Receiver sends an ACK
Assume the frame to be lost, if ACK is not received within a predefined timeout.

## Slide 61: Virtual Carrier Sensing (VCS) – CSMA/CA
Image Source: Asymmetric RTS/CTS for Exposed Node Reduction in IEEE 802.11 Ad Hoc Networks
Request to Send (RTS)
Clear to Send (CTS)

## Slide 62: Setting up Network Allocation Vector (NAV)
Image Source: https://community.arubanetworks.com/t5/Technology-Blog/Understanding-802-11-Medium-Contention/ba-p/232034

## Slide 63: IEEE 802.11 Distributed Coordination Function (DCF)
Set n = 0 /*n denotes the round number*/
Use PCS (and VCS) to sense the channel
If the channel is busy, repeat 2
If the channel is idle for DIFS duration, transmit the frame, set timeout
If ACK received within timeout, Go to 1
If timeout, set CWmin = min (2xCWmin, CWmax)
Set n = n+1
Set CW = random (0, CWmin)
Wait for CW number of slots and go to 2