## Slide 1: CS 31006: Computer Networks – Moving From End-to-End To Per Hop

## Slide 2: What We Have Learnt So Far …
The design of current network architecture is based on experience and requirements
Physical
Physical
Data Link
Physical
Data Link
Network
Physical
Data Link
Network
Transport

## Slide 3: What We Have Learnt So Far …
Software, Kernel
Firmware, Device Driver
Hardware
Physical
Data Link
Network
Transport
Application
Protocol stack is implemented across different layers of the operating system

## Slide 4: Network (Internet) Layer Services
UDP
End to end packet delivery
TCP
Connection Establishment
Reliable Data Delivery
Flow and Congestion Control
Ordered Packet Delivery
Transport
Data Link
Network
Addressing
Routing
Datagram delivery (unreliable)

## Slide 5: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
SW Lab 1
SW Lab 2
Router
CSE Network

## Slide 6: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
CSE Network
EEE Network
SW Lab 1
SW Lab 2
EE Lab 1
EE Lab 2
IITKGP Network

## Slide 7: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
IITKGP Network
IITBBS Network
EEE
CSE
EEE
CSE
ERNET Network

## Slide 8: Internet Architecture – Basic Principles
Internet is organized in a hierarchical fashion.
BSNL Network
IITKGP
IITBBS
BSNL Public
BSNL Corporate
Bharti Airtel Network
ERNET Network

## Slide 9: Internet Architecture
Autonomous Systems (AS) – A set of LANs for an administrative domain, identified by a unique AS number, and the routing policies are controlled by a single administrator.
Local Area Network (LAN) – A set of devices with a common layer 3 gateway

## Slide 10: Autonomous System Graph for India
Source: https://labs.apnic.net/vizas/#IN

## Slide 11: Internet Architecture
Internet Service Providers (ISP) – An AS provides Internet connectivity to another group of ASes or end users

## Slide 12: Peering between ISPs

## Slide 13: Communication between Two Nodes over ISPs

## Slide 14: IP Addressing – Basic Principles
We need to forward data packets from one network to another network via different intermediate networks.
AS 10
AS 11
AS 13
AS 12
Host 1
Host 2

## Slide 15: IP Addressing – Basic Principles
The address should identify a network as well as a host inside a network
AS 10
AS 11
AS 13
AS 12
Host 1
Host 2

## Slide 16: IP Addressing
Divide the address space (32 bit in IPv4) among network address and host address
The old age – Classful addressing: Fixed number of bits for network address and host address
Network address
Host address

## Slide 17: Classful Addressing
How to identify a class – use the first few bits
  0 – Class A, 10 – Class B, 110 – Class C, 1110 – Class D, 1111 – Class E

## Slide 18: Network Address and Broadcast Address
Network address – identify a network
  All 0’s in the host address part
  Ex-1 (Class A): 01111110.00000000.00000000.00000000 (126.0.0.0)
  Ex-2 (Class B): 10111101.11101001.00000000.00000000 (189.233.0.0)
Broadcast address – send the data to all the hosts of a network
  All 1’s in the host address part
  Ex-1 (Class A): 01111110.11111111.11111111.11111111 (126.255.255.255)
  Ex-2 (Class B): 10111101.11101001.11111111.11111111 (189.233.255.255)
How many valid hosts can be there in a Class A, in a Class B and in a Class C IP address?

## Slide 19: Subnetting and Supernetting – Classless Inter-domain Routing (CIDR)
You have 255 hosts in a network. Which IPv4 address class will you use – Class C or Class B ?
  Class C – not possible
  Class B – huge address space is lost (using only 255 addresses out of possible 216-2 addresses)
Split a large network or combine multiple small networks for efficient use of address space
  Subnetting – divide a large network into multiple small networks
  Supernetting – combine multiple small networks into a single large network
Subnet mask – denote the number of bits in the network address field

## Slide 20: Divide a Network into Subnets

## Slide 21: CIDR – Addressing Format
Host Address
Subnet Address
We write the IP address as 191.180.83.235/12 in CIDR notation
  The first 12 bits are the network address and rest (32-12)=20 bits are for host address
The subnet mask is 255.240.0.0
10111111
10110100
01010011
11101011
11111111
11110000
00000000
00000000
IP Address
Netmask

## Slide 22: CIDR - Manual IP Setting in the OS

## Slide 23: Divide a Network into Subnets
Let the IP address of a network is 203.110.0.0/16
We want to divide this network into three subnets
We need 3 bits for subnets – why not 2 bits?
  Subnet 1 – 100, Subnet 2– 101, Subnet 3 – 110
Rest 13 bits are used for addressing the hosts of those subnets.
The subnets are – 203.110.128.0/19, 203.110.160.0/19, 203.110.192.0/19

## Slide 24: All Zero and All One Subnets
192.168.0.0/16
192.168.0.0/17
192.168.128.0/17
192.168.0XXXXXXX.X
192.168.1XXXXXXX.X
The network address for the subnet and the original network is identical – Subnet Zero
Broadcast address for this subnet is 192.168.255.255, broadcast address for the original network is also 192.168.255.255 – All-One Subnet
We normally avoid “all zero” and “all one” subnets.

## Slide 25: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19

## Slide 26: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts

## Slide 27: CIDR Example
Address space – 203.110.0.0/19
  13 bits are available to serve all the hosts of IITKGP network
  We need to divide these address space among 3 subnets
CSE – 11 bits, VGSOM – 9 bits, EE – 9 bits for host address
We have 2 bits left for identifying three subnets – Is this possible?
  Avoid “all zero” and ”all one” subnets
Let us apply CIDR – Combine VGSOM and EE Networks together

## Slide 28: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts

## Slide 29: CIDR Example
CSE – 11 bits, VGSOM+EE – 10 bits
Network address – 203.110.0.0/19, 203.110.000XXXXX.XXXXXXXX
CSE network address 203.110.00010XXX.XXXXXXXX (203.110.16.0/21)
VGSOM+EE network address 203.110.00001XXX.XXXXXXXX (203.110.8.0/21)

## Slide 30: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts
203.110.16.0/21
203.110.8.0/21

## Slide 31: CIDR Example
VGSOM – 9 bits, EE – 9 bits
Network address – 203.110.8.0/21, 203.110.00001XXX.XXXXXXXX
VGSOM network address 203.110.0000110X.XXXXXXXX (203.110.12.0/23)
EE network address 203.110.0000101X.XXXXXXXX (203.110.10.0/23)

## Slide 32: CIDR Example
CSE – 2000 Hosts
VGSOM – 500 Hosts
EE – 500 Hosts
203.110.0.0/19
11 bit hosts
9 bit hosts
9 bit hosts
10 bit hosts
203.110.16.0/21
203.110.8.0/21
203.110.12.0/23
203.110.10.0/23

## Slide 33: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.3.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.4.0 | 255.255.255.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Routing Table for R1

## Slide 34: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.3.0 | 255.255.255.0 | 172.16.2.2 | eth1
10.0.4.0 | 255.255.255.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Routing Table for R1
Compaction of routing table is possible

## Slide 35: CIDR – Routing Table Construction
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
Network | Netmask | Gateway | Interface
10.0.0.0 | 255.255.0.0 | 172.16.2.2 | eth1
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Compact
Routing Table for R1

## Slide 36: CIDR – Problem of Multihoming
10.0.2.0/24
10.0.3.0/24
10.0.4.0/24
R1
R2
R3
eth0
eth1
10.0.2.1/24
10.0.3.1/24
10.0.4.1/24
172.16.1.1/24
172.16.1.2/24
172.16.2.1/24
172.16.2.2/24
eth2
172.16.3.1/24
172.16.3.2/24
10.0.4.2/24

## Slide 37: CIDR – Longest Prefix Match
Network | Netmask | Gateway | Interface
10.0.0.0 | 255.255.0.0 | 172.16.2.2 | eth1
10.0.4.0 | 255.255.255.0 | 172.16.3.2 | eth2
0.0.0.0 | 0.0.0.0 | 172.16.1.1 | eth0
172.16.1.0 | 255.255.255.0 | 172.16.1.1 | eth0
172.16.2.0 | 255.255.255.0 | 172.16.2.2 | eth1
Supernetting is not always perfect !
There is always a possibility of duplicate entries
Where to forward 10.0.4.8 ?

## Slide 38: CIDR – Longest Prefix Match
Use Patricia Tree (a compact representation of trie) for matching prefixes.
0
1
00
10
11
100
101
00*
0*
11*

## Slide 39: Next, we’ll look how to construct the routing table for the Internet …